PART 2 - PRODUCTS

2.1	TURFGRASS SOD:

        - Description: Bluegrass Sod suitable for sand based sports fields, lawns and gardens of uniform density, color, and texture, strongly rooted, and capable of vigorous growth and development when planted.

        - Sod specifications include but are not limited to:

- Shall be grown from a 5 seed blend utilizing at least 3 highly-rhizomatous cultivars that exceed normally accepted industry criterion.  Shall be rated highly wear-tolerant, have strong living color, be disease resistant, with strong leaf texture and early spring and late fall green color.

- Shall contain no rye grass cultivars.

- Shall have a maximum 50# per acre seeding rate.

- Shall have a minimum one year root base with strong rhizome development.

- Shall be certified noxious weed free.

- Shall be Water Wise TurfTM.

  - Shall require no more than 30” annual supplemental water during establishment and no more than 20” annual supplemental water after establishment.

  - Shall contain a strong root base capable of root penetration to a minimum depth of 8” into landscape soil.

- Growing medium shall be a sandy soil (75% sand, 17% silt, 8% clay) with low clay content.

- Shall be grown without netting.

- Shipping mow height shall be 1-1/2”.