PART 2 - PRODUCTS

2.1	TURFGRASS SOD:

        - General Information

          - Provide bluegrass sod that is certified, approved, Number 1 Quality/Premium, including limitations on thatch, weeds, diseases, nematodes, and insects, complying with TPI's "Specifications for Turfgrass Sod Materials" in its "Guideline Specifications to Turfgrass Sodding."

          - Furnish bluegrass sod suitable for native soils, sports fields, lawns and gardens of uniform density, color, and texture, strongly rooted, and capable of vigorous growth and development when planted.

        - Bluegrass  Sod

- Sod specifications include but are not limited to:

  - Shall be grown from a 5 seed blend utilizing at least 3 highly-rhizomatous cultivars that exceed normally accepted industry criterion.  Shall be rated highly wear-tolerant, have strong living color, be highly disease resistant, with strong leaf texture and early spring and late fall green color.

  - Shall contain no rye grass cultivars.

  - Shall have a maximum 50# per acre seeding rate.

  - Shall have a minimum one year root base with strong rhizome development.

  - Shall be certified noxious weed free.

  - Shall be Water Wise TurfTM.

    - Shall require no more than 30” annual supplemental water during establishment and no more than 20” annual supplemental water after establishment.

    - Shall contain a strong root base capable of root penetration to a minimum depth of 8” into landscape soil.

  - Growing medium shall be a sandy loam soil with low clay content with proven meld capability with pga grade sand growing base.

  - Shall be grown without netting.

  - Shipping mow height shall be 1-1/2”.