PART 2 - PRODUCTS

2.1	TURFGRASS SOD:

        - Description: Royal Blue ProTM Bluegrass Sod suitable for native soils, sports fields, lawns and gardens of uniform density, color, and texture, strongly rooted, and capable of vigorous growth and development when planted.

        - Royal Blue ProTM  sod specifications include but are not limited to:

- Shall be grown from a 5 seed blend utilizing at least 3 highly-rhizomatous cultivars that exceed normally accepted industry criterion.  Shall be rated highly wear-tolerant, have strong living color, be highly disease resistant, with strong leaf texture and early spring and late fall green color.

- Shall contain no rye grass cultivars.

- Shall have a maximum 50# per acre seeding rate.

- Shall have a minimum one year root base with strong rhizome development.

- Shall be certified noxious weed free.

- Shall be Water Wise TurfTM.

  - Shall require no more than 30” annual supplemental water during establishment and no more than 20” annual supplemental water after establishment.

  - Shall contain a strong root base capable of root penetration to a minimum depth of 8” into landscape soil.

- Growing medium shall be a sandy loam soil with low clay content with proven meld capability with pga grade sand growing base.

- Shall be grown without netting.

- Shipping mow height shall be 1-1/2”.

- Shall be supplied by Chanshare Farms – 10785 W. 12800 N., Tremonton, UT 84337.